## Slide 1
Server
Server App
  Android app for Bluetooth communication between U3 and ZigBee
  Configuring nodes
    To local / remote nodes
      Set GPIO mode
      Read GPIO values
      Read AI values
      Set report mode (sampling / change)
      Set GPIO values
    Scan ZigBee devices
  Server for controlling the nodes
    HTTP server
    JSON RPC between server and client
U3
Bluetooth
BT-ZigBee
Combo
Bluetooth
ZigBee
(Coordinator)
Device
ZigBee
(Device)
Switch, Relay
TCP
Server

## Slide 2: Configuring Nodes
Coordinator / Router / End-Device
  AT+NT=0, 1, 2, 3, 4
  0=none, 1=coordinator, 2=router, 3=end-device, 4=sleepy end-device
For coordinator, Permit Joining
  AT+PJ=255 (or sec)
Node name
  AT+NN=<value> (up to 16 chars)
Scanning
  AT+AS : scan network
  AT+ES : scan energy of the channels
  AT+DS : scan nodes in the current network
  AT+RS : showing RSSI and LQI RSSI=-100~+127dBm, LQI=0~255

## Slide 3: Configuring GPIOs
Mode setting
  AT+GPIO<number>=<value>
  0=disabled, 1=DIN, 2=DOUT(low), 3=DOUT(high), 4=AIN (9~14), 5=reserved
In / Out
  AT+DIO? or AT+DIO<number>?
  AT+DIO=<value> or AT+DIO<number>=<value>
Analog
  AT+AI? or AT+AI<number>?
  출력값을 실제 측정된 전압값으로 변환
    출력값이 0 ~ 7FFF 인 경우, Voltage (mV) = Value * 0.1
    출력값이 8000 ~ FFFF 인 경우 Voltage (mV) = (Value – 65536) * 0.1
  온도센서에서 실제 측정된 전압값을 온도로 변환
    Temperature(℃) ={ Volt(mV) -600(mV)} * 0.1(℃/mV)
  조도센서에서 실제 측정된 전압값을 조도로 변환
    Illumination(Lux) = Volt(mV) * 0.25(Lux/mV)

## Slide 4: Configuring GPIOs
Periodic Sampling
  AT+DL=<IEEE address>
  ATS42=<value> Sampling period (sec)
  ATS43=<value> 0 for DL, 1 for Sink node
  ATZ
  Data format : ++<IEEE address>|<GPIO value><CR>
Change Detection Sampling
  AT+DL=<IEEE address>
  ATS43=<value> 0 for DL, 1 for Sink node
  ATS44=<value> 0 for not using sampling
  ATZ

## Slide 5: Configuring BT-ZigBee Combo
Configuring as Coordinator
  AT+NT=1
  AT+NN=BT_ZIGBEE_COMBO
UI
  Configuring Node
    Node Type
    Node Name
  Configuring GPIO
    GPIO NO, PIN NO, MODE

## Slide 6: Client App
Query the devices
  Showing the devices configured by Server App
Attributes are shown as Icon
  Switches (R/W)
  Volume (R/W)
  Remote Control (R/W)
  Temperature (R)
  Luminance (R)
Send control and receive current status
Rule making
  On, Off, Toggle rules

## Slide 7: Apparatus
Pan & Tilt Gimbal for FPV
  160 degree with Gimbal
  Phone is attached to the gimbal
  PWM signal is used for rotating the phone
Power
  Charger is used
  Power is distributed to both BT-ZigBee combo and Phone
USB Charger Plug
BT ZigBee

## Slide 8: Schematic